## Slide 1: Lecture 25: Input/Output Technology
HW2 due Sunday GR5 (final implementation) out Today is the last nanoquiz of the term!

## Slide 2: UI Hall of Fame or Shame
Notes: From Ryan Young:
“While using the Xbox program 'Xbox FTP Client', I stumbled upon this alternative to the tried-and-true approach. The letters are placed like those on a phone pad, three letters and a number to each box. The left analog stick is used to select the box, and the right analog stick is used to highlight the letter/number of your choosing. Once the appropriate glyph is highlighted, you pull the right trigger with your index finger (a very natural motion, with both thumbs resting on the analog sticks) to select the letter/number. Once familiar with the interface, I've found I can type my name ("ryan young") in about 20 seconds, whereas it takes about 50 seconds with a traditional cursor and keyboard combination.”
natural mapping
external consistency

## Slide 3: Nanoquiz
closed book, closed notes
submit before time is up (paper or web)
we’ll show a timer for the last 20 seconds

## Slide 4
In which of the following situations would animation be likely to help? (choose all that apply) A. Highlighting a button (to show that it’s enabled) when the user mouses over it B. Scrolling when the user clicks on a link to another place in a document C. Displaying a throbber D. Scrolling when the user drags the scrollbar thumb.
jQuery’s animate() method is usually called from an event listener; for example, a click listener might use animate() to animate the appearance of a menu. Which of the following statements are true as a result? (choose all that apply) A. animate() uses timer events. B. animate() uses mouse capture. C. animate() doesn’t return until the animation is complete. D. animate() contains a loop that steps through the frames of the animation.
Which of the following techniques is most useful for animating a fast-moving object? (choose the best answer) A. motion blur B. slow-in, slow-out C. anticipation D. follow-through
20
19
18
17
16
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
Notes: Note that 2(a) might be false if jQuery uses CSS3 Animation.

## Slide 5: Today’s Topics
Displays
Pointing devices

## Slide 6: CRT vs. LCD

## Slide 7: Properties of Displays
Diagonal size
Pixel dimensions & aspect ratio
Pixel density
Refresh rate
Color depth (# colors or grays)
Color gamut
Gamma

## Slide 8: Pixel Dimensions
Notes: how CRTs can make pixels larger or smaller by changing frequency of scan (analog resampling), but LCD pixels are fixed
display’s natural resolution always looks sharpest
square vs. nonsquare pixels

## Slide 9: Pixel Density
Pixels per inch (ppi)
  CRT, LCD: 60-130 ppi
  iPhone 4: 326 ppi
  Laser printer: 300-1800 ppi
Lines per inch (lpi) for halftoning
  Newspaper: 85 lpi
  Magazine: 133 lpi
  Art book: 200 lpi
Notes: Note that DPI and PPI are sometimes used confusingly – sometimes the quoted “dpi” for an LCD panel is actually three times its true ppi, because they’re counting the three subpixels
Smartphone PPI: http://pocketnow.com/index.php?a=portal_detail&t=news&id=4341
Lines per inch refers to number of halftone grid lines per inch. Digital halftoning uses a subgrid of pixels instead of different sizes of dots. So for 100 shades of gray, you’d need 10x10 pixel grid squares, so a 600 ppi printer would only be able to get 60 lpi halftoning.
So a bad rule of thumb is to multiply the lpi by 10 to find the equivalent ppi. Magazine printing using digital halftoning can be up to 2500 ppi!

## Slide 10: Subpixel Rendering on LCDs
Ideal for text
  kerning
  boldface
  italic
But only horizontal text
Subpixel rendering
Notes: Subpixel rendering takes this a step further. Every pixel on an LCD screen consists of three discrete pixels side-by-side: red, green, and blue. So we can get a horizontal pixel density which is three times the nominal pixel density of the screen, simply by choosing the colors of the pixels along the edge so that the appropriate subpixels are light or dark. It only works on LCD screens, not CRTs, because CRT pixels are often arranged in triangles, and because CRTs are analog, so the blue in a single “pixel” usually consists of a bunch of blue phosphor dots interspersed with green and red phosphor dots. You also have to be careful to smooth out the edge to avoid color fringing effects on perfectly vertical edges. And it works best for high-contrast edges, like this edge between black and white. Subpixel rendering is ideal for text rendering, since text is usually small, high-contrast, and benefits the most from a boost in horizontal resolution. Windows XP includes ClearType, an implementation of subpixel rendering for Windows fonts. (For more about subpixel rendering, see Steve Gibson, “Sub-Pixel Font Rendering Technology”, http://grc.com/cleartype.htm)

## Slide 11: Electronic Paper
Electrophoretic display
  charged white particles in a dark-colored oil
  made by E Ink
  used by Amazon Kindle & Sony Reader
Only consumes power to change display
Low refresh rate (1-2 Hz), low contrast
Kindle is 167 ppi, 16 levels grayscale
Notes: white particles are titanium dioxide (about a micron in size)

## Slide 12: Multiple Monitors and Very Wide Displays
Multiple monitors are increasingly common
Microsoft DSharp prototype
  made with 3 LCD projectors = 3072 x 768 pixels
  curved, 48” wide, 12” high, 4:1 aspect
Problems with multiple monitors
  losing mouse pointer
  clutching
  bezels & seams
  locus of attention

## Slide 13: Projectors
LCD projector
  basically LCD panel with very bright backlight
DLP (“digital light processing”)
  uses a digital micromirror device instead of LCD

## Slide 14: Today’s Topics
Displays
Pointing devices

## Slide 15: Pointing Devices
Mouse
Touchpad
Joystick
Trackball
Notes: Mouse
Touchpad
Trackpoint
Trackball
Focusing on indirect pointing devices today – Friday’s lecture will say more about direct touch on the screen

## Slide 16: Properties of Pointing Devices
Direct vs. indirect
  Direct touch on screen
  Indirect control of mouse pointer
Relative vs. absolute
Throughput
Control/display (C/D) ratio
Notes: more about direct touch on Friday
mouse vs. trackball: Mackenzie et al. “A Comparison of Input Devices in Elemental Pointing and Dragging Tasks.” CHI 1990.
mouse vs. trackball vs. touchpad vs. joystick: MacKenzie et al, “Accuracy Measures for Evaluating Computer Pointing Devices”, CHI 2001.
http://www.yorku.ca/mack/CHI01.htm

## Slide 17: Throughput
Throughput
  also called index of performance
  mouse: 5 bits/sec
  trackball: 3 bits/sec
  touchpad: 3 bits/sec
  joystick: 2 bits/sec
T = a + b log (D/S + 1) seconds
ID = log (D/S + 1) bits
IP = 1/b bits/second

## Slide 18: Control/Display Ratio
Control: how far user’s hand moves
  in meters
Display: how far cursor moves on screen
  in pixels
Direct touch: C/D = 1
Mouse acceleration
No acceleration
With acceleration

## Slide 19: Semantic Pointing
Adapt the C/D ratio to the targets on screen
  Highly likely targets have high C/D ratio => pointer moves more slowly, target feels sticky
  Less likely targets have low C/D ratio => pointer moves fast, slips over them
“Look” is unchanged
...but “feel” is different
Notes: Blanch et al. “Semantic pointing: improving target acquisition with control-display ratio adaptation.” CHI 2004.
demo at http://www.infres.enst.fr/~blanch/projects/SemanticPointing/demo/

## Slide 20: Direct Touch
Mouse = indirect pointing
Stylus or finger = direct pointing

## Slide 21: Technology for Direct Touch
Resistive
  Two conductive sheets with a gap between
  Responds to finger, stylus, any object
Capacitive
  Human skin changes surface capacitance
  Responds only to bare skin
Inductive
  EM field from tablet induces signal from stylus
  Responds only to special (expensive!) stylus
Optical
  Camera watches the surface
  Responds to anything

## Slide 22: Resistive Touch Sensing

## Slide 23: Resistive Touch Sensing
1 V

## Slide 24: Resistive Touch Sensing
2 V

## Slide 25: Resistive Touch Sensing
Stripped Wire

## Slide 26: Resistive Touch Sensing
Stripped Wire

## Slide 27: Resistive Touch Sensing
3 V
Stripped Wire

## Slide 28: Resistive Touch Sensing

## Slide 29: Resistive Touch Sensing

## Slide 30: Resistive Touch Sensing
3 V

## Slide 31: Resistive Touch Sensing
3 V
3

## Slide 32: Resistive Touch Sensing
3

## Slide 33: Resistive Touch Sensing
2 V
3

## Slide 34: Resistive Touch Sensing
2 V
3
2

## Slide 35: Resistive Touch Sensing

## Slide 36: Resistive Touch Sensing

## Slide 37: Resistive Touch Sensing

## Slide 38: Resistive Touch Sensing
75%

## Slide 39: Resistive Touch Sensing
75%

Fast
Accurate
Finger or Stylus

## Slide 40: Resistive Touch Sensing
75%

Fast
Accurate
Finger or Stylus
Not Multi-touch


## Slide 41: Capacitive Touch Sensing

## Slide 42: Capacitive Touch Sensing
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-

## Slide 43: Capacitive Touch Sensing
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-

## Slide 44: Capacitive Touch Sensing
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
20 C
20 C
20 C
20 C

## Slide 45: Capacitive Touch Sensing
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
20 C
20 C
20 C
20 C

## Slide 46: Capacitive Touch Sensing
20 C
20 C
20 C
20 C
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-

## Slide 47: Capacitive Touch Sensing
19 C
17 C
17 C
15 C
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-

## Slide 48: Capacitive Touch Sensing
19 C
17 C
17 C
15 C
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-

## Slide 49: Capacitive Touch Sensing
19 C
17 C
17 C
15 C
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-

## Slide 50: Capacitive Touch Sensing
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-

## Slide 51: Capacitive Touch Sensing
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-

## Slide 52: Capacitive Touch Sensing
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
90%

## Slide 53: Capacitive Touch Sensing
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
90%
Bare Finger or Conducting Stylus
Not multi-touch

## Slide 54: Projected Capacitive Touch Sensing
Multi-touch

## Slide 55: Inductive Touch Sensing

## Slide 56: Inductive Touch Sensing
EM Field

## Slide 57: Inductive Touch Sensing

## Slide 58: Inductive Touch Sensing

## Slide 59: Inductive Touch Sensing

## Slide 60: Inductive Touch Sensing
?

## Slide 61: Inductive Touch Sensing
Expensive 

Not Multi-touch

## Slide 62: Vision Touch Sensing

## Slide 63: Vision Touch Sensing

## Slide 64: Vision Touch Sensing
Light is faster through air than glass,
so it over-shoots and heads back into glass

## Slide 65: Vision Touch Sensing
Light is slower through a finger than glass,
and the finger diffuses the light

## Slide 66: Vision Touch Sensing

## Slide 67: Vision Touch Sensing

## Slide 68: Vision Touch Sensing

## Slide 69: Vision Touch Sensing
Infrared

## Slide 70: Vision Touch Sensing

## Slide 71: Microsoft Surface

## Slide 72: DiamondTouch Table (MERL)
Notes: designed for multiple users around a tabletop
rotation becomes an important issue
multiple users (and multiple touches per user) are identified by an array of transmitting antennas in the surface and sensors connected to their chairs
front-projected (because the antenna array is presently opaque), so occlusion of the display is worse

## Slide 73: Issues for Direct Touch Technology
Finger only, stylus only, or both
Pressure sensitivity
Hovering vs. clicking
Occlusion of display by finger or hand
  “Fat finger” problem
Multitouch
Tactile feedback
Multiple users

## Slide 74: Summary
Displays
  CRT, LCD, e-paper, projector
  Dimensions, density, refresh rate, color depth
Pointing devices
  Mouse, touchpad, joystick, trackpad
  Throughput, C/D ratio
Keyboards
  QWERTY, Dvorak, alphabetical
  Typing speed, finger movement