## Slide 1: SMA 5505
Applied Parallel Computing

## Slide 2: Plan
Parallel computers
  Basic architecture
Parallel programming
  Message-passing
  Shared-memory
Parallel algorithms
  Numerical
  Non-numerical
Paper readings


## Slide 3: Summary of previous lecture
Q: What is parallel computing?
A: Part of nature;
Q: Why go parallel?
A: No choice– as we approach the limits of sequential processing
  Several measures of speedup
  Amdahl’s law & its correct interpretation

## Slide 4: Outlines for today’s:
Q: How different are parallel computers from sequential computers
A dose of parallel architectures useful for efficient use of parallel computers
Q: How to go parallel?
A: divide+ communicate+ synchronize

## Slide 5: Contents
Architectures
  Taxonomy
  Processors &
  communications infrastructure
Parallel programming paradigms
  Correctness: deadlocks, non-determinism, …
  Efficiency:
    communications cost
    (a priori / a posteriori analysis)

## Slide 6: Architectures
Flynn’s taxonomy:
  Instruction Stream Data stream
SISD: Single Instruction, Single Data
SIMD: Single Instruction, Multiple Data
MISD: Multiple Instruction, Single Data
MIMD: Multiple Instruction, Multiple Data

## Slide 7: SISD
serial, scalar (von Neumann) computer
A single instruction issued / clock cycle
Each instruction operates on a single scalar data element
Performance: # instructions issued/unit time
  MIPS (million of instructions per second),
  MFLOPS (million Floating-point OPerations) for eng/scientific applications

## Slide 8: SIMD
Multiple functional units within an instruction processor
A single instruction issued/clock cycle
Each instruction operates on multiple data elements
Synchronous, lock-stepped operations
Performance:
  # instructions issued /unit time and
  # functional units
Main applications: eng/scientific
MFLOPS
CM2 (Connection Machine 2)

## Slide 9: SIMD with chained functional units

## Slide 10: SIMD with replicated functional Units
ALU
a1
a2
a3
a4
a5
a6
b1
b2
b3
b4
b5
b6
c2
c6
c1
C =A+B
control
IR
+
c3
c4
c5

## Slide 11: MISD
Multiple processors working on the same data stream
Few but interesting
E.g. pipelined processing of
  graphics
  video streaming
More special-purpose
Will be useful when processors are easily reconfigured.

## Slide 12: MIMD
Multiple instruction processors  multiple instructions may be executed /clock cycle
Each processor executes independently on own data elements
  Multiple SIMD: asyn among multiple SIMDs, syn. within a SIMD (Fujitsu VP, Cray 2); MFLOPS
  Multiple SISD: asyn. at processor level ; MIPS & MFLOPS
top 500: All ASCI machines, Intel Paragon, IBM SP2, CM5, etc

## Slide 13: Multiple SIMDs  MIMD

## Slide 14: Multiple SISD  MIMD
x=300;
.
.
.
z= x*y;
call A(z, n);
…
.
x=300;
.
z= x*y;
call A(z, n);
DO 5 I =1, N
c= a+b;
.
.
.
May execute different programs;
Even if executing same program, may work at different instructions

## Slide 15: Architectures
Modified Classification
SISD Single processor | SIMD Array processor
MISD Processor pipelines | MIMD Multi-processor
asynchronous
synchronous
Single data stream
multiple data stream

## Slide 16: Architecture of Processors for Parallel Computers:
How different is a parallel processor from a sequential processor?
A short answer:
Custom-made  Very different
Commodity  no difference

## Slide 17: Economics: Commodity vs custom-made
time
Performance/price
Custom-made: always has higher performance, but also high cost;
occupies niche market
Quantum jumps caused by innovative designs

## Slide 18: Commodity vs custom-made
time
Performance/price
Commodity: started after successful market;
low cost, low performance
quality improves steadily with volume;
- Curve relatively smooth
thru smaller but continuous improvement
- May grow faster than linear;
Driven by popular demand:

## Slide 19: Economics: Commodity vs custom-made
time
Performance/price
I
II
iii
However, here quantity wins-
along with quality!
“wonders of technology”
If Quantity wins over Quality:
tyranny of the mob
iv
Rate of increase of commodity goods is
normally greater for the size of market

## Slide 20: Rest In Peace: (source: Gordon Bell)

## Slide 21: Beowulf:
• best price performance
  $28 per sustained MFLOPS
  $11 per peak MFLOPS  how do you beat this?!
• rapid response to technology trends
• no single-point vendor
• just-in-place configuration
• scalable
• leverages large software development investment
• mature, robust, accessible
• user empowerment
• meets low expectations created by MPPs from Thomas Sterling

## Slide 22: Do we have a choice? AOL Server Farm (source: Gordon Bell)

## Slide 23: A commodity PC (Parallel Computer) (source: Gordon Bell)
Processors are not a problem!
So what is the problem?  how to connect them?

## Slide 24: Processors:
Can zoom into custom-made supers if time allows.
Performance-cost ratio: moving towards commodity processors  commodity processors (= SISD processors!)
For parallel processing, major improvements needed:
communications-related operations: instruction processor design  benchmarking of parallel applications  resources to devote

## Slide 25: Architecture for Communications (hardware):
processor
(a). Shared Memory: common address space
processor
processor
Interconnection network
memory
memory
memory
memory
…
…
Shared common memory
All memory locations equally accessible by all processors
 Communication reduced to accessing common memory
 Easy to learn programming
cache
cache
cache

## Slide 26: Communications Architecture (hardware):
(a). Shared Memory
UMA: All memory locations equally accessible:
 difficulty in building large int. network <= 32 processors
NUMA: Non-uniform access time
easier to scale (larger shared-memory systems- SGI)

## Slide 27: Communications Architecture
processor
(b). Distributed Memory: share nothing
processor
processor
Interconnection network
memory
memory
memory
…
…
Local and remote memory modules
 non-uniform cost of access: easier for hardware implementation
 Explicit communications: Processors send/receive data via network
supports abstraction: Message Passing
cache
cache
cache

## Slide 28: Infrastructures for communications:
Interconnection networks:
  1. Commodity:
  Lower Performance
  Cheaper: e.g. Beowulf
  e.g. bus, Ethernet, ATM switch, Fast Ethernet, Giga-bit network
  2. Custom-made:
  High performance
  Expensive (most supers: CM5; SP2)
  switched, multi-stage network: cross-bar, Omega, …
  direct-connection networks: linear, mesh, hypercube, etc

## Slide 29: Interconnection networks:
EXAMPLE
Commodity networks
Ethernet/Fast Ethernet/Gbps Ethernet
How it works:
Cost: sending O(1)-sized data on a fixed network
Point-to-point: O(1) on average (worst is O(p) )
Broadcast: O(1) time

## Slide 30: Communication cost vs Compute cost
Yesterday:
  10 MBps (100 Mbps Ethernet)
  ~20 MBps tcp/ip saturates 2 cpus
  round-trip latency ~250 µs
Now
  Wires are 10x faster Myrinet, Gbps Ethernet, ServerNet,…
  Fast user-level communication
    tcp/ip ~ 100 MBps 10% cpu
    round-trip latency is 15 us >> time for a compute operation
1.6 Gbps demoed on a WAN

## Slide 31: Custom-made networks:
EXAMPLE
Switched networks (Multi-stage Networks) (Indirect networks)
Cost of communication can be accounted from number of stages
Butterfly network
Point-to-point
Broadcast:

## Slide 32: Custom-made networks:
EXAMPLE
Direct networks (Interconnection topologies)
processor
cache
memory
Linear array
1D torus
=
Communication ports

## Slide 33: Network topology
Perhaps the most interesting & versatile:
N-cube

## Slide 34: Are interconnection networks relevant? Yes, when scaling up…

## Slide 35: Each node could be anything:

## Slide 36: Sample network topology:
2D mesh

## Slide 37: Network topology
2D torus variation 1

## Slide 38: Network topology
2D torus variation 2

## Slide 39: Network topology
3D Mesh
Matches exactly with the 3D grids

## Slide 40: Network topology
Fascinating:
Trees, fat-trees, mesh-of-trees, pyramids, etc.
Network of Blue Mountain:
http://research.microsoft.com/users/GBell/SCphotos_files/frame.htm

## Slide 41: Network topology

## Slide 42: Network topology

## Slide 43: Interconnecting…
To form a computer grid:
node : a computer, a cluster or sub-network, etc.
Links: communication channels
Connect them as a mesh? Linear array?
What are the criteria for choosing one?

## Slide 44: How to compare Interconnection Networks?
Node degrees: #links/node  complexity of the network interface  overall cost
Regularity: how uniform the topology  easier to replicate HW/SW
Versatility/universality: Emulation of other topologies (embedding)
Scalability: add or delete nodes; Incremental changes
Fault-tolerance: reconfigure/bypass the faulty nodes
Network diameter:  worst case of point to point communication
Bisection width: maximal concurrency allowed;
Routing efficiency:
  Point-to-point
  Broadcasting
  Multicasting
  All-to-all
Ease of designing communication algorithm

## Slide 45: Linear Arrays:
N nodes
Network diameter: N-1
Node degrees: #links/node = 1 OR 2
Regularity: non-uniform topology  easier to replicate HW/SW (special cases at the end)
Versatility/universality: hard to embed linear arrays, mesh, trees, etc. (dilation/congestion will result)
Scalability: easy to add or delete nodes;
Bisection width: 1
Routing efficiency: Point-to-point: ON) Broadcasting: N) Multicasting: N) All-to-all: N)  how?

## Slide 46: Mesh:
Dimension d  N= Ld nodes
Network diameter: (N)1/d
Node degrees: #links/node = d
Regularity: uniform topology  easier to replicate HW/SW
Versatility/universality: Embedding of linear arrays, mesh, trees, etc.
Scalability: add or delete nodes;
Bisection width: (an exercise)
Routing efficiency: Point-to-point: N1/d ) Broadcasting: N1/d ) Multicasting: N1/d ) All-to-all: N)  how?

## Slide 47: n-Cube
Dimension n  N= 2n nodes
Network diameter: lg N
Node degrees: #links/node = lgN
Regularity: uniform topology  easier to replicate HW/SW
Versatility/universality: Embedding of linear arrays, mesh, trees, etc.
Scalability: add or delete nodes; scale by a factor of 2
Bisection width: 
Routing efficiency: Point-to-point: lgN) Broadcasting: lgN) Multicasting: lgN) All-to-all: N)
Ease of designing communication algorithm

## Slide 48: Interconnection networks
They are the real thing to support communications among processors
All communications in the software will have to be supported thru the communication infrastructure.
Many algorithms have been designed to exploit the structural properties of the interconnections: e.g. routing, sorting, .. Even matrix operations. (see, e.g. Leighton’s book)

## Slide 49: Interconnection networks
Quite important when scaling up any system:
Even Beowulves will have to be scalable--
What to do? Simply use routers? How are the routers connect to each other?
Current research issues:
Different technologies for optical networks, wireless networks, etc.
Geographically wide spread nodes 
High cost of connection need to have sparsity and some regularity in connections.

## Slide 50: Summary:
A simplified overview of parallel architecture
Processors and Interconnects are being researched intensively
Can zoom in for the motivated/interested