## Slide 1
Simulation of a Parallel Computing Routing Algorithm for IP/DWDM network
MOY Group:
Ma Keng Teck (smap1079)
Ou Hanyan (smap1050)
Yu Jia (smap1062)

## Slide 2: Outline
Overview
IP/DWDM Network Design and Optical Routing Algorithms (By Yu Jia)
IP Network Routing with ILP solver and network topology generation (By Hanyan)
Optical Communication Protocol and GUI (By Ma Keng Teck)
Demo

## Slide 3: Why optical?
Handle increase in IP traffic
  Moore’s law doesn’t apply here
  1984: 50Mbps, 2001: 6.4Tbps~10Tbps/fiber
Reduce cost of transmitting a bit
  Cost/bit down by 99% in last 5 years
Enable new applications and services by pushing optics towards the edges

## Slide 4: Internet Reality
SONET
Data
Center
SONET
SONET
SONET
DWDM
DWDM
Data
Center

## Slide 5: Fiber capabilities/DWDM
Wavelengths can be time-division multiplexed into a series of aggregated connections
Sets of wavelengths can be spaced into wavebands
Switching can be done by wavebands or wavelengths
1 Cable can do multi terabits/sec

## Slide 6: Our Competitor: WDM GURU, OPNET Technology, Inc (Nasdaq OPNT)
http://www.opnet.com/products/wdmguru/home.html

## Slide 7: WDM GURU, OPNET
1.Generating Revenue
2.Optimizing Capital Investment
3.Reducing Operating Costs
4.Reducing Risk
Our goal !
Enable service providers and network equipment manufacturers to design resilient, cost-effective optical networks

## Slide 8: Our Approach
Use parallel machine to simulate the routing behavior about 70,000 routers. (This limit is actually given by the machine memory we have)
Support LINUX and UNIX, while OPNET supports Windows NT/2000.

## Slide 9: Our Approach (cont.)
Compute routes covering IP networks and Optical Network, while WDM GURU supports Optical Network only.
We have similar GUI with OPNET
Our simulation considers communication cost, while sequential versions don’t.

## Slide 10: Implementation details:
We used 14 processors on a cluster machine to simulate 14 IP networks, each of which is connected to 14 OXC nodes.
Each IP network is composed of 5000 routers or clients.

## Slide 11: Implementation details:
Each processor controls 1 OXC equipment and knows the 14-node optical network topology.
The request may cover different networks. Typical one is IP network Optical network  IP network
Parallel wavelength reservation (use MPI)

## Slide 12
IP/DWDM Network Design and Optical Routing Algorithms
Yu Jia

## Slide 13: Network Design (By Yu Jia)
It’s not a pure computation problem, and we hope to obey to the IP network and Optical Network constraints.
1. Network Data Structures, O-O (Object Oriented) :
Router, OXC, Link, Fiber(optical), Path, LightPath, IP Network, Optical Network, etc.
2. IP Network and Optical Network Initialization.

## Slide 14
3. Compute routes in Optical Network:
Use DIJKSTRA algorithm, Priority Queue, etc to find shortest path. If we need to find backup disjoint path, just remove the links in the primary path and compute a secondary path.

## Slide 15
4. Maintain and update the resource information in the IP network and Optical Network.
  Before computing a request, scan through the data to remove the links that don’t have enough bandwidth or wavelength, and assign costs to links.
  After each request, store the lightpath to the OXC to save recomputing for next request which uses same destination OXC.

## Slide 16: Maintain Lightpath in Edge Router
bandwidth
Source, Dest
Request
Router
Outgoing Port
Dest-network
Path
Lightpath Table
Routing Lookup Data Structure
Router 1
Router 11
Router 14
Path1 (G,R,w)
Path 2 (G,R,w)
Path4(G,R,w)

## Slide 17
5. Lazy Release of resources: put the active requests to queues which use same ligthpath. Whenever a new request comes in and request using this lightpath, OXC will check the timestamps of the requests stored in the queue. If they are outdated, delete them.

## Slide 18
IP Network Routing with ILP solver and network topology generation
Ou Han yan

## Slide 19: IP layer topology generation
Generate random topology for each IP network on each node.
Requirements for topology:
Each edge is bidirectional.
Every pair of nodes have a path.

## Slide 20: Routing request type
For requests on each node, there are two types:
Local request: source and destination are in one IP net.
  One local request = one IP request
Global request: source and dest are in two IP net
  One global = two IP requests+one Optical request
We generate random requests !

## Slide 21: Routing in parallel
Routing in IP network in parallel
  Translate global requests to local requests
  Each node calculate its local requests independently
Routing in Optical network in parallel
  Calculate lightpaths independently
  Using SWAP to communicate and coordinate

## Slide 22: Routing in IP network (if Sequential)
Suppose 100 global requests from IP net 1 to IP net 2
Routing in IP network in sequence
  Deal with requests one by one
Subnet 1
Subnet 2
LightPath
OXC
OXC

## Slide 23: Routing in IP network
Suppose 100 global requests from IP net 1 to IP net 2
Routing in IP layer in parallel
  Deal with requests in parallel
Subnet 1
Subnet 2
OXC
OXC
LightPath

## Slide 24: Routing in IP network in parallel
How to route the IP requests in parallel
Send the global requests destination to according nodes.
Receive the global requests destination from other nodes and translate to local IP.
Each node calculates the routing path for local requests in parallel.

## Slide 25: Routing in IP network using ILP
Use ILP to solve routing problem in IP layer
Why?
  ILP is more flexible than shortest path.
  We want to get the optimal paths.

## Slide 26: Routing in IP network using ILP
Routing can be formulated as the following ILP problem:
Object:
Constraints:

## Slide 27: Routing in IP network using ILP
If we want to find one primary path and one backup path.
Object:
Constraints:

## Slide 28: Routing in IP network using ILP
At first, we want to use parallel ILP solver.
  No free parallel ILP solver.
Use free sequential ILP solver(its author:Michel Berkelaar).
  But this ILP solver can’t run on every node.
  Must make the solver run on each node to calculate in parallel

## Slide 29: Routing in IP network using ILP
One method to make ILP solver run on each node:
  Write a shell script like:
  #!/bin/sh
  ssh compute-0-0 ./lp_solve < ./test0.lp
  ssh compute-0-1 ./lp_solve < ./test1.lp
  ssh compute-0-2 ./lp_solve < ./test2.lp
  ...

## Slide 30: Routing in IP network using ILP
Another method to make ILP solver run on each node:
  Modify the source code of the ILP solver.
  Make the ILP solver as a module of our program.
  Fortunately, we succeed in this method.

## Slide 31
SWAP (Simple Wavelength Assignment Protocol)
Ma Keng Teck

## Slide 32: Implementation Details: (NSF network topology)

## Slide 33: Wavelength-continuity Constraint
In the absence of wavelength conversion devices (too expensive), a lightpath must occupy the same wavelength on each link in its route.
RWA: Routing + Wavelength Assignment
  Static
  Dynamic
We applied dynamic lightpath establishment with parallel wavelength reservation!

## Slide 34: Wavelength Routing
4
1
3
2
5
Lightpath on
wavelenth 1
Lightpath on
wavelenth 2
Lightpath on
wavelenth 3

## Slide 35: SETUP
2 phase protocol
1st phase: SETUP
  SENDER :
    Reserved Free Wavelength Set
    Send Reserved Wavelength Set
  Intermediate:
    Own’s Free Wavelength Set  Received Reserved Wavelength Set
    Reserved new set of Wavelengths
    Send the new set to next in route
Notes: The source node attempts to reserve the desired wavelength on each link in the route by sending a separate control message to each node in the route. Each node that receives a reservation request message will attempt to reserve the specified wavelength, and will send either a positive or negative acknowledgment back to the source. If the source node receives positive acknowledgements from all of the nodes, it can use this wavelength and communicate with the destination.

## Slide 36
  RECEIVER :
    Choose 1 wavelength from Received Free Wavelength Set
    Send COMMIT to previous node in route
2nd phase: COMMIT
  Intermediate
    Relay back committed Wavelength
    Clear Reserved Wavelengths
    Set Wavelength as COMMITED
  Sender
    Same, but can start sending

## Slide 37
Release
  Relay RELEASE Message
  Release COMMITTED Wavelengths

## Slide 38: Implementation
Coded in MPI
Use MPI to simulate control messages in network

## Slide 39: Graphical User Interface
Java Interface
Communicate via Unix Pipe

## Slide 40
Demo
Q&A